## Slide 1: Robot Manipulator
University of Windsor
Electrical and Computer Engineering Department
Mechatronics and Robotics Lab (MRL)
By: Nesrine Awad and Saeed Mozaffari
2021

## Slide 2: Outline
Loop
SubProg
Assignment
If
Script
Event
Thread
Switch
Timer
Home

## Slide 3: Loop
A loop can be used for program code that is to be repeated several times in a row.
The program code that must be repeated is placed inside a loop command.
The loop can be configured to repeat infinitely, a specific number of times, or as an expression is true based on a variable or an input.

## Slide 4: Example
Let us create a simple program with three waypoints that repeats our commands from waypoint 1 to waypoint 2 five times; then moves onto waypoint 3.
1) To begin, select Loop from the Advanced menu.
2) Click on Loop X times.
3) Click on the blank Loop count space and type in 5 to have it repeat five times.
4) From the Basic tab and add in our first two waypoints: Waypoint_1 and Waypoint_2.
5) Set each waypoint position, for Waypoint_1 let us have it start from a higher point and make Waypoint_2 a position below that so we can see our robot move up and down.

## Slide 5: Example
6) Now, click on Robot Program at the beginning to insert another waypoint out of the loop.
7) Let’s add Waypoint_3 and set it to move to the left.
You have now successfully created a program that loops through Waypoint_1 and Waypoint_2 five times before moving on the Waypoint_3.

## Slide 6: SubProgram
A SubProgram can hold program parts that are needed several places.
A Sub Program can be a separate file on the disk and be used in other programs.
A call to a sub program will run the program lines in the sub program, and then return to the following line.
A subprogram can be called based on a value of a variable or an input from an external device.

## Slide 7: Example
Let us create a SubProgram_1 and call it when variable Count is equal to 1.
In the program tree, click the command line after which you want to call a subprogram.
In the node list, click Advanced tab.
Click SubProg.
Click the Command tab.
Select Create New in the dropdown menu.
Enter new program data in the subprogram.

## Slide 8: Example

## Slide 9: Assignment
The Assignment command assigns values to variables.
This can be useful in complex programs.
The variables can also be set by operator.

## Slide 10: If
If command is used for parts of the program that is only be executed if a certain condition is true, e.g. a sensor inputs or variable.
If the condition is evaluated as True, the statements within If command are executed, otherwise the robot execute the commands in the else statement.
An If command can have several ElseIf statements that can be added and removed using the Add ElseIf and the Remove ElseIf buttons.

## Slide 11: Example
We want the robot to move to Waypoint_1 if a variable is True and move to Waypoint_2 if it is False.

## Slide 12: Script
Apart from using the teach pendant, we can use robot script programming which enables us to program a robot on a host computer and just sending commands via an Ethernet socket connection to the robot.
Typically programming languages such as C++, Java, Visual Basic, and Python can be used for script programming .

## Slide 13: Event
With Event command an action is executed in parallel to main program when a selected condition is accomplished.
An event is similar to interrupt, however, in an event the execution of the main program continues while the event code is being executed.
An event can be used to monitor an input signal and perform some action or set a variable when that input signal goes high.

## Slide 14: Example
We want the robot to turn on the conveyor if the sensor is high, wait for 10s and then turn off the conveyor.

## Slide 15: Thread
A Thread is a parallel process to the robot program and can be used e.g. to control an external machine independently of the robot arm.
A thread can communicate with the robot program with variables and output signals.

## Slide 16: Example
We want to write a thread to check the input from sensor and turns the conveyor on and off based on the input from the sensor. The thread should be repeated every 0.1 second.

## Slide 17: Switch
A Switch Case command can make the robot change behavior based on sensor inputs or variable values.
Each Switch can have several Cases and one Default Case. Cases can be added or removed using the buttons on the screen.
If the condition is evaluated to match one of the cases, the lines inside the Case are executed. If a Default Case has been specified, then the lines will be executed only if no other matching cases were found.

## Slide 18: Example
Let’s create a program that has 3 cases possible: Default case, Case 1 and Case 2. We will set it to execute Case 1 if the value is 1, and Case 2 if the value is 2. If the value is neither of these, we will set it to Default Case.
Start by selecting Assignment and then in the Source menu select Operator.
Click Request the operator for: and then select a whole number and enter the number 1.
Next, select Switch in the Advanced tab.
4) Click on the + Case to add Case 1 and then click it again to insert Case 2.
5) Click on the + Case again to add another Case, but this time select the Default Case box so that this one becomes our Default Case.

## Slide 19: Example
6) In the Switch yellow box for each Case, select Variable from the menu and select var_1

## Slide 20: Timer
To measure the time the Timer command can be used.
We can start, stop, or reset the timer in our program.

## Slide 21: Example
Let’s set a timer to start at the beginning of the program to inform us how long it took to execute.
1) To start, let’s add in and set Waypoint_1, Waypoint_2 and Waypoint_3.
2) Select Timer, timer_1, and add it into the beginning of the program tree. Select Start.
4) Copy the timer to the bottom of the program tree and select Stop.

## Slide 22: Example
5) Run the program.
6) If you go into the Variables tab, you will see timer_1 has a value with the number of seconds it took to successfully complete the program.

## Slide 23: Home
With Home command, we can move the robot to the Home Position defined in the installation step.
The movement speed and time can be set.

## Slide 24: Rights of use
This is shared under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International Public License