## Slide 1: Robot Manipulator
University of Windsor
Electrical and Computer Engineering Department
Mechatronics and Robotics Lab (MRL)
By: Nesrine Awad and Saeed Mozaffari
2021

## Slide 2: Outline
Power On
Move
Installation
I/O Tab
Rename I/O
Safety Boundary
Safety Limits
Log
Run
Program

## Slide 3: Power On
We need to start by pushing the Power On button of the teach pendant.
The powering on will initialize the polyscope allowing us to control the robot.
There will be a loading period, wait until the process has finished and a window will appear.

## Slide 4: Power On
Click on Program Robot and then select the red circle at the bottom.

## Slide 5: Power On
Select ON (This will change the state of the robot to Idle and enables power to the joints of our robot).

## Slide 6: Power On
Next, select START (This will change the state from Idle to Normal and releases the mechanical brakes).
Then click Exit.

## Slide 7: Degree of Freedom (DoF)
The robot we are using is a 6-axis robot, meaning it has 6 degrees of freedom of movement.
The joints of the robot are named 0, 1, 2, 3, 4 and 5, or also known as Base, Shoulder, Elbow, Wrist 1, Wrist 2 and Wrist 3.

## Slide 8: Move
Click on the Move tab and you will see a screen that has several functions.

## Slide 9: Move
The purpose of this screen is to move the robot during programming to know where the joints are located (visible on the degree of position and the X,Y,Z indicator).
There are six arrow keys that represent each joint, which can be moved using the arrow bars.
Underneath the first six arrows, you will see “Combination” arrows, which move several joints simultaneously so that a linear move can be made during programming.

## Slide 10: Move
The robot has a natural home position. The Move screen has a “Home” button.
Pressing the Home button will bring you to a “Move Robot into Position” screen.

## Slide 11: Move
This will allow us two choices: Auto move or manual move.
If Auto move is selected, the robot will move by itself to the home position, but we must keep our finger pressed on the button until the move is complete.
If there seem to be obstacles in your pathway that the robot can crash into, you may want to select a manual move.
To do this, press the manual button which will bring you to the main move screen, allowing you to have full control and move the robot safely.
If at any point you move the robot beyond its joint limitations, you will encounter a pop-up error that says, “Joint Limitation Violation”, which is a safety stop. Press “Enable Robot” to continue and acknowledge the error.

## Slide 12: Installation
In the installation tab, you will see a menu with:
-General
-Safety
-Features
-Fieldbus
All these menus can be expanded by tapping on them.

## Slide 13: Installation
Under general, TCP is your Tool Center Point, and you can see the position and orientation.
You can also set the Payload and edit the Home position from this menu.

## Slide 14: I/O Tab
I/O’s are the connectors in the control box of the robot that transfer signals between other devices such as sensors, PLC’s and scanners.
The purpose of this tab is to allow us to see the signal state (HIGH/LOW) of the inputs and outputs. This tab allows us to manually control the inputs and outputs.
The robot has 8 digital inputs and 8 digital outputs on the controller board as well as 2 analogue inputs and 2 analogue outputs inside the cabinet. The tool head also has 2 digital outputs and 2 analogue inputs.

## Slide 15: I/O Tab
Click on the Installation tab, then select the I/O tab.
In the I/O tab screen, the input and outputs are displayed, and the output values can be changed by clicking on them.

## Slide 16: Rename I/O
To rename an I/O, go to the Installation tab.
Select General, and then select I/O Setup.
Click on the input or output that you want to rename.
Type in the new name for the I/O.

## Slide 17: Rename I/O
You can also rename the I/O’s to make it easier for programming. (ex: change name of “digital input 4” to “sensor” so its purpose is clear.)

## Slide 18: Safety Boundary
A safety boundary is useful for triggering the robot to work in a reduced mode or for preventing the robot from working in specified areas.
A safety boundary can be set by clicking on the Installation tab.
Next, select Safety from the menu. If there is a password set for your robot, unlock it by entering the safety password.
You will see a Planes tab, select Add plane.

## Slide 19: Safety Boundary

## Slide 20: Safety Boundary
Under Copy Feature, choose which feature you want to link the safety plane with. (ex: Undefined, Base, Point_1).
Next, in Restrictions you will select the restriction you want to affix to the safety plane. (ex: Normal, Reduced, Both, Trigger Reduced Mode).
Select Apply, then you will select Apply and restart.
Final step for your safety boundary is to select Confirm Safety Configuration.

## Slide 21: Safety Limits
General limits can be customized in safety settings. General limits have four positions which range from “very restricted” to “least restricted”.

## Slide 22: Safety Limits
When these settings are changed, they cause the force, speed, power and momentum to either increase or decrease according to the selection.
To adjust the general limits, we will select Safety from the Installation tab.
Next, enter the safety password if you need one and select Unlock.
Select the Robot Limits tab and use the slider to choose the settings you prefer.
Select Apply, then you will select Apply and restart.
Final step for your general safety limits is to select Confirm Safety Configuration.

## Slide 23: Log
The log tab will show a log screen, which shows useful information regarding the status of the robot and controller.

## Slide 24: Log
Some of the information found in log includes:
-power supply output
-joint status
-controller temperature
-consumption
At the bottom of the screen is a running system log which shows the information of recent activities. This is useful for troubleshooting purposes.

## Slide 25: Run
The Run tab allows you to load a program that you have already written and saved, or one of the default programs.
Underneath the run tab, you will also see the robot’s age.

## Slide 26: Program
The program tab is where you will write your program for the robot. We will discuss all the Basic and Advanced commands you can use later.

## Slide 27: Rights of use
This is shared under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International Public License