## Slide 1: Robot Manipulator
University of Windsor
Electrical and Computer Engineering Department
Mechatronics and Robotics Lab (MRL)
By: Nesrine Awad and Saeed Mozaffari
2021

## Slide 2: Outline
Waypoint
Move
Direction
Wait
Set
Popup
Comment
Halt
Folder

## Slide 3: Waypoint
A basic robot program consists of waypoints and motion between the waypoints.
A waypoint specifies the location the robot moves to.
By clicking the Move button, a motion and a waypoint are inserted in the program tree.
By clicking the waypoint, we can set the location,
rename it, or change the robot speed at this waypoint.

## Slide 4: Set Waypoint
The ? symbol in the move here box means that the waypoint has not been set yet.
To set it, click set waypoint and move the robot by the arrow key.

## Slide 5: Waypoint Position
There are three methods to specify the position of a waypoint and tell the robot arm where to be: Fixed position, Relative position, Variable position.

## Slide 6: Fixed Position
A fixed position waypoint is given by physically moving the robot arm to the position.

## Slide 7: Relative Position
A relative position waypoint is related to the robot arm’s previous position, such as “two centimeters to the left”. The relative position is defined as the difference between the two given positions (left to right).
The distance here is the Cartesian distance between the TCP in the two positions. The angle states how much the TCP orientation changes between the two positions. More precisely, the length of the rotation vector describing the change in orientation.

## Slide 8: Variable Position
A waypoint with the variable position is given by a variable.
The variable has to be a pose variable with 6 components. The first three are x,y,z and the last three are the rotation around x,y,z axis.
For example, to move the robot 20 mm along the z-axis of the tool, we can use var_1=p[0,0,0.02,0,0,0].

## Slide 9: Movement Types
When the robot moves from one waypoint to another, the operator can choose the motion type to get from one waypoint to another.
The motion type determines the path or trajectory the robot moves through when moving to the waypoint.
There are three different move types: MoveJ, MoveL, and MoveP.

## Slide 10: MoveJ
moveJ makes movements that are calculated in the robot arm joint space.
This movement type is used when it is desired to have the robot arm move fast between waypoints, disregarding the path of the tool between those waypoints.
Each joint is controlled to reach the desired end location at the same time. This movement type results in a curved path for the tool.
The shared parameters that apply to this movement type are the maximum joint speed and joint acceleration.

## Slide 11: MoveL
moveL moves the robot linearly between waypoints on a straight line path.
We can set the desired tool speed, tool acceleration, and a feature.
The selected feature will determine in which feature space the tool positions of the waypoints are represented in.

## Slide 12: MoveP
moveP moves the tool linearly with constant speed with circular blend radius. It is desirable for some process operations, like gluing or dispensing.
A smaller blend radius value will make the path turn sharper whereas a higher value will make the path smoother.
While the robot arm is moving through the waypoints with constant speed, the robot control box cannot wait for either an I/O operation or an operator action. Doing so might stop the robot arm’s motion, or cause a protective stop.

## Slide 13: Shared parameters
The shared parameters in the bottom right corner of the Move screen apply to the movement from the previous position of the robot arm to the first waypoint under the command, and from there to each of the following waypoints.
The Move command settings do not apply to the path going from the last waypoint under that Move command.

## Slide 14: Example
Using what we just learned, let’s insert a relative waypoint.
1) Click the Move button (select either moveJ, moveL or moveP). Let’s use moveP for our example.

## Slide 15: Example
2) Click on the Waypoint that was inserted when you made your move selection.
3) Click the Command tab and select the Relative position.

## Slide 16: Example
4) In the from point area, click set point and define your starting point to record the offset. Repeat this for the to point area to record the offset.
Now your relative waypoint has been inserted and defined.

## Slide 17: Direction
The Direction tab will insert an option under a Move, which allows the robot to move in a linear movement that is relative to the selected feature.
In this tab, you will see the options of Direction: Base or Tool
There is also the option to select Direction from X+, X-, Y+, Y- or Z+, Z-.

## Slide 18: Direction
You can also pick type in the direction vector.
There is also an option to delete the “until” feature or use it to specify a stop condition such as an expression, distance, tool contact or I/O input.

## Slide 19: Example
Let’s set a X+ Direction with a distance of 400 mm.
1) Start by selecting Direction from the Basic menu.
2) Click Direction: Base and select Base under Feature and X+ under Direction.
3) Select Until, and then select Distance. Type in 400 to finish your direction setting.

## Slide 20: Wait
Wait command pauses I/O signal, or expression, for a given amount of time.
The robot can wait for a fix time, or for a digital input to be high or low.
Also, the robot can wait for an analog input to reach a certain amount of a function of different inputs.

## Slide 21: Example
Let’s use a wait command in our program. Let’s insert a 5 second wait period.
1) In the program tree, click Waypoint and select moveJ.
2) Next, click on the Waypoint that was inserted and set your waypoint.
3) Next, under the Basic menu, select Wait.
4) Select what trigger you want for the robot’s next action. Your options are: No Wait, Wait ___ seconds, Wait for Digital input ___, Wait for Analogue input ______, or Wait for f(x). For our example, we will select the Wait ___ seconds.

## Slide 22: Example
5) When you click on blank seconds space, a pop-up window appears where we can select the length of time. Type 5 seconds and click the green check mark to confirm.
Now your 5 second wait has been successfully added into the program tree.

## Slide 23: Set
With set command we can set either digital or analog outputs to a given value. For example, a conveyor can be turned on or off with this command.
The command can also be used to set the payload of the robot arm when the weight at the tool differs from the expected payload. This prevent the robot from triggering a protective stop.

## Slide 24: Example
Let’s use a set command to set our Digital Output “4” to “High”.
1) In the program tree, click Waypoint and select moveJ.
2) Next, click on the Waypoint that was inserted and set your waypoint.
3) At this waypoint, we will add our set command. To do this, under the Basic menu, select Set.

## Slide 25: Example
4) Configure the output to the new value you want to add. Your options are: No action, Set digital output ___, Set analogue output ___, Set output ___ f(x), Set Single Pulse ___ and Increment installation by one: ____. For our example, we will select Set Digital Output ___. Click the Digital Output area to choose digital_out[4].

## Slide 26: Example
5) Next, select the tab that says “low” and change it to “HIGH”.
This will successfully set our Digital Output 4 to High. You can view it in the program tree as DO[4]=On.

## Slide 27: Popup
The popup is a message that appears on the screen and the robot waits for the operator to press the “OK” button before continuing the program.

## Slide 28: Example
Let’s add a pop-up message that says “hello world” into our program.
1) To do this, under the Basics tab, select Popup.
2) Click on the Command tab and then enter the text into the blank yellow space.

## Slide 29: Example
3) Type in hello world.
4) You can select if you want to view this as a message, a warning or an error.
For our example, we will select Message.
Your popup has now been set. Run the program to see the pop-up message.

## Slide 30: Halt
The program execution stops at this point.

## Slide 31: Comment
Comment gives the programmer an option to add a line of text to the program.
This line of text does not do anything during program execution.

## Slide 32: Example
Let’s add a comment that says “starting point” into our program.
1) To do this, under the Basics tab, select Comment.
2) Click on the Command tab and then enter the text into the blank space.

## Slide 33: Example
Let’s add a comment that says “starting point” into our program.
1) To do this, under the Basics tab, select Comment.
2) Click on the Command tab and then enter the text into the blank space.
Your comment is now inserted into the program tree.

## Slide 34: Folder
A Folder is simply a collection of program lines. It is used to make the program easier to read and navigate.
Folders have no impact on the program and its execution.

## Slide 35: Folder
A Folder is simply a collection of program lines. It is used to make the program easier to read and navigate.
Folders have no impact on the program and its execution.

## Slide 36: Example
Let’s add two folders for a Pick and Place program. The first folder will be titled Pick and the second folder will be titled Place.
1) To do this, under the Basics tab, select Folder.
2) Click on the Command tab and then click the space titled Folder and insert your text, “Pick”.
3) Click the green checkmark button to submit.

## Slide 37: Example
4) Add another folder following the same previous steps.
5) Insert your text, “Place”.
6) Click the green checkmark button to submit.
You’ve now created your folders for a Pick and Place program where you can put in separate commands. You can select Hide Folder program Tree on the bottom to keep things neatly organized when the program becomes full of commands.

## Slide 38: Rights of use
This is shared under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International Public License