## Slide 1: Robot Operating System (ROS)
University of Windsor
Electrical and Computer Engineering Department
Mechatronics and Robotics Lab (MRL)
By: Saeed Mozaffari
2021

## Slide 2: Outline
Creating workspace
Creating a package
ROS topic
ROS service
ROS action

## Slide 3: Programming with ROS
In the previous part we discussed the basics of the Robot Operating System.
Now, we focus on programming with ROS which provides us some built-in functions to implement ROS capabilities.
For example, to implement a new ROS topic, or a new ROS message, we can simply call these ROS built-in functions to create it. We don’t need to implement ROS features from scratch.
C++ and python are two common languages for ROS programming.

## Slide 4: Creating a ROS Workspace
For ROS programming, first we need to create a ROS workspace.
ROS workspace is a place where ROS packages are kept.

## Slide 5: Creating a ROS Workspace
For workspace creation, we build a folder called catkin_ws, inside of which is another folder called src.
After creating these folders, switch to the src folder.
To create and build the packages properly, we should initialize the workspace with the following command:
catkin_init_workspace

## Slide 6: Creating a ROS Workspace
After initializating the workspace, the CMakeLists.txt file is created inside the src folder.
We should go back to workspace folder and build the workspace with catkin_make command.

## Slide 7: Creating a ROS Workspace
After building the workspace we have several folders in the catkin_ws.

## Slide 8: Creating a ROS Workspace
src Folder:
  It is the place where you can create, or clone new packages from repositories.
build Folder:
  It includes cache files that prevent from rebuilding previous packages when running the catkin_make command for a new package.
devel Folder:
  If the package build process is successful, the target executable is created and stored inside the devel folder.
  The following command should be added to the .bashrc file, so that we can access the workspace packages in all terminal sessions.

## Slide 9: Creating a ROS Workspace
To add the workspace path to the .bashrc file to the following:

## Slide 10: Creating a ROS Workspace
To change the workspace from default one to our created catkin_ws, add its path to the .bashrc file.

## Slide 11: Creating a ROS Package
After creating the ROS workspace, we can create a ROS package, where for each project, ROS nodes, libraries etc. are organized there.
First, go to the src folder in the catkin_ws.
Then, run catkin_create_pkg which has two parameters.
The first parameter is the package name, and the second one is dependencies of the package.

## Slide 12: Creating a ROS Package
This figure shows the output of catkin_create_pkg command.
Inside of the my_first_ros_pkg package we have two files (Cmakelists.txt, package.xml) and one folder (src).
Finally, compile the workspace with catkin_make command.

## Slide 13: Creating a ROS Package
CMakeLists.txt:
  This file has all the commands to build the ROS source code inside the package and create the executable.
package.xml:
  This XML file contains the package dependencies, and other information.
src Folder:
  The source code of ROS packages are kept in this folder.
  Normally, C++ files are kept in the src folder.
  If you want to keep Python scripts, you can create another folder called scripts inside the package folder.

## Slide 14: Creating a ROS Node
A node is an executable that uses ROS to communicate with other nodes.
To create a node, we should do the following tasks:
ROS Modules:
  when you write Python code, the first section imports Python modules.
  Assume we want to import python module and string message type.

## Slide 15: Creating a ROS Node
Initializing a ROS Node:
  Before starting any ROS node, the node should be initialized with rospy.init_node.
  It has two arguments. The first argument is the name of the node, and the second argument shows if the node can run on multiple instances or not.
Printing Messages in a ROS Node:
  ROS provides APIs to log messages. These messages are readable string that convey the status of the node.

## Slide 16: Example
Create a node and deactivate it when user press Ctrl+c.

## Slide 17: Nodes Communication
There are three different methods that nodes can exchanging messages.
Topic (Asynchronous):
  It provides a unidirectional message transmission/reception.
  Topics are used when continuous exchanging data is required.
Service (Synchronous):
  It provides a bidirectional message request/response.
  Unlike the topic, the service is onetime message communication (only when there is a request).
Action (Asynchronous):
  It provides a bidirectional message goal/result/feedback.
  Actions are used when it is difficult to use the service due to long response times.

## Slide 18: Nodes Communication

## Slide 19: Topics in ROS
As topics are unidirectional and remain connected to continuously send or receive messages, it is suitable for sensor data that requires publishing messages periodically.
Multiple subscribers can receive message from a publisher and vice versa.

## Slide 20: Example
We want to create two nodes, talker and listener, which communicate with each other through chatter topic.
The type of message in the topic is string.

## Slide 21: Example
Creating Publisher Node:
Creating Publisher Object:
  After creating the publisher node, its object can be created by rospy.Publisher command which has three arguments (topic name, message type, and queue size).
  The queue size determines the size of subscriber message buffer.

## Slide 22: Example
Defining publishing frequency:
Defining the message:
Publishing the message:

## Slide 23: Example

## Slide 24: Example
To run the code and see the result, the following commands should be run in separate terminals.

## Slide 25: Example
Let’s build a python file for the subscriber in the same package, and do not forget to make it executable.
Creating Subscriber Node:
  After initializing the subscriber node, run rospy.publisher command which has three arguments (topic name, message type, and callback function).
  Notice that the topic name and message type should be the same as the publisher.
  The callback function is automatically executed when the subscriber receives a new message.

## Slide 26: Example
Defining the Callback Function:
  In the callback function we want to print the received message.
The Spin Function:
  It is used to keep the node exiting until the node has been shutdown.

## Slide 27: Example
To run the code and see the result, the following commands should be run in separate terminals.

## Slide 28: Example
The topic nodes are shown below.

## Slide 29: Example
The subscriber file is shown below.

## Slide 30: Services in ROS
A service consists of a server that responds only when there is a request and a client that can send requests as well as receiving responses.
When the request and response of the service are completed, the connection between two nodes will be disconnected.
A service is often used to command a robot to perform a specific action or nodes to perform certain events with a specific condition.

## Slide 31: Example
We want to create two nodes, server and client, which communicate with each other through add-two-ints service.
The client sends two integers to the server and the server sends back their summation.
We want to use AddTwoInts service message which is available in rospy_tutorials.

## Slide 32: Example
Create my_server.py file in my_service package.
ROS Modules:
  imports Python modules and messages.
Creating Server Node:
  After initializing the server node, its object can be created by rospy.Service command which has three arguments (service name, service type, and handle function).
  When there is a new request, handle function is executed.

## Slide 33: Example
Service Type:
  We can see the service type using rossrv show command.
Handle Function:

## Slide 34: Example
The server file is shown in the following:

## Slide 35: Example
Let’s check the service.

## Slide 36: Example
Creating Client Node:
  First, the client should wait for the server to be available before sending its arguments.
  Next, we create a handle for calling the service.
  To show the error if the server is not available, we use try except command in python.

## Slide 37: Example
The client file is shown in the following:

## Slide 38: Example
It is important to note that unlike the server node, the client node is terminated after receiving the service (why?).

## Slide 39: Actions in ROS
Action is used when responding to a requested takes a long time to be completed.
It has three messages: goal, result, and feedback.
The goal and result correspond to request and response messages in service, respectively.
The feedback message is used is added to report progress to the client periodically when intermediate values are needed.
Actions are suitable for performing complex robot tasks which are time-consuming, and the client does not have to be idle until receiving the response from the server.

## Slide 40: Actions in ROS

## Slide 41: Example
We want to create an action that returns Fibonacci series.
We want to create two nodes, server and client, which communicate with each other through an action.
The client sends and integer to the server to calculate Fibonacci series to that order.

## Slide 42: Example
Creating the package:

## Slide 43: Example
Creating Action Server:
  Build a folder with the name of scripts and create an executable python file with the name of my_server in it.

## Slide 44: Example
  We defined feedback and result messages.
  Creating the action server.
  Starting the server.
  Calculating Fibonacci series and publishing it in the feedback message.

## Slide 45: Example
  Defining feedback and result messages.

## Slide 46: Example
The server file is shown in the following:

## Slide 47: Example
Creating Action Client:
  Defining callback functions:
  Creating the action client.

## Slide 48: Example
  Creating goal message.
  Sending the goal message.

## Slide 49: Example
The client file is shown in the following:

## Slide 50: Rights of use
This is shared under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International Public License