## Slide 1: Robot Manipulator
University of Windsor
Electrical and Computer Engineering Department
Mechatronics and Robotics Lab (MRL)
By: Nesrine Awad and Saeed Mozaffari
2022

## Slide 2: Outline
Seek
Force
Palletizing
Conveyer Tracking

## Slide 3: Seek
The Seek feature is useful for stacking and destacking parts.
This allows us to not have to count the parts that are being placed in a stack as the robot will be able to seek down until it finds the top of the stack and pick up the part from there.
Four parameters should be set: A (the starting position),
B and C (FromPos and ToPos) which show the direction, and
D (the item thickness).
It should be noted that the direction is the opposite to the robot movement. For example, in stacking action, which requires the robot to move from top to bottom, FromPos is lower than ToPos.

## Slide 4: Seek
By selecting Stacking from the two options shown in seek command, we should set some parameters such as item thickness, when the next position should be found, starting position (StartPos_1), Direction of the stack (Direction), and sequence of actions at each position (PlaceSequence).

## Slide 5: Seek
When we select the item thickness, the robot knows the next item position on the stack.
By defining when the next position should be found, the robot knows when to restart the stacking.
FromPos and ToPos locations determines the stacking direction and their exact locations are not important. For example, in the stacking application, the FromPos should be lower than the ToPos.
For PlaceSequence we can set the StackPos as the StartPos.
We can set some outputs or wait for a specific amount of time between stacking items.
Finally, we can set the Exit point to avoid robot collision with stacked items.

## Slide 6: Example
Write a program to pick objects from the conveyor and stack them using seek command.

## Slide 7: Force
For certain tasks, you might want to adjust the robot to apply a specified force.
We can use the force template to apply a force in the Z direction of a feature, apply force in more than one direction, or to apply force towards a specific point.

## Slide 8: Example
Let us create simple force program that applies a force of 5N in the Z direction.
To begin, select Force from the Templates menu.
Select Simple from the drop-down menu.
Next, let’s enter the amount of force desired in the blank space. For our example, let’s type in 5 Newtons.
Select Test to make sure it is applied correctly. If you want to go in the negative direction adjust the 5 to a -5.
Your force has been successfully set.

## Slide 9: Palletizing
Palletizing is useful for packaging, teaching the robot how to pick and place items from areas and perform the same actions for different items.
The robot will then automatically place the work piece according to the pallet pattern defined by the operator.
This feature also allows us to create palletizing programs with multiple layers, separators for in-between the layers, and different patterns.

## Slide 10: Palletizing
The operator can change the name of pallet.
For multiple layer palletizing, the height of objects is required.
Robot can save the number of handled items and location of the last item.

## Slide 11: Palletizing
Items can be palletized in three different patterns: line, grid, and irregular.
Based on each pattern, location of items on the pallet should be defined.
Also, a separator can be added between layers. In this case, height of separator should be determined.

## Slide 12: Palletizing
By clicking layers, we can add more layers for palletizing.
Layers are stacked in Z-direction of the base feature.
The first layer is always the bottom most layer.

## Slide 13: Palletizing
By clicking At Each item, we can define where the robot can approach and exit and also the type of actions needed for each item (ToolActionPoint).

## Slide 14: Palletizing
By clicking At Each item, we can define where the robot can approach and exit and also the type of actions needed for each item (ToolActionPoint).
There is no need to repeat these actions for each item on the pallet. We define the actions at the first item of the first layer in the palletizing sequence which is called the ReferencePoint.

## Slide 15: Example
Write a program to pick up items from a conveyor and put them on a pallet. Use thread to control the conveyor.

## Slide 16: Conveyer Tracking
When using the conveyer tracking option, the robot will adjust its movement to follow the movement of conveyer.
In this case, all robot movements are allowed while tracking the conveyer, but they are relative to the motion of the conveyer belt.

## Slide 17: Rights of use
This is shared under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International Public License