## Slide 1: Mobile Robot
University of Windsor
Electrical and Computer Engineering Department
Mechatronics and Robotics Lab (MRL)
By: Sooraj Sunil
2022

## Slide 2: Outline
Connecting to QCar
Manual Driving
Obtaining Lidar Scans Data
Save and Load Lidar Data
SLAM in ROS
Visualize the Map (rviz)
SLAM in MATLAB
Visualize the Map (plot)

## Slide 3: Connecting to QCar
1) The QCar platform can be used directly as a computer, complete with a 6-core CPU, an NVIDIA GPU, a built-in speaker, microphones and an extensive sensor suite. Connect a keyboard/mouse using the provided USB ports, and connect up to 2 monitors using the HDMI ports on board.

## Slide 4: Connecting to QCar
2) For applications that require the platform to be moving or require remote access, a direct setup is not feasible. In such cases we use a wireless setup with the Ground Control Station (GCS).
The QCar is configured to automatically connect to the router through wireless connection.
the LCD on the QCar shows a wireless symbol as well as the IPv4 address of the platform dynamically assigned by the provided router.

## Slide 5: Connecting to QCar
We can use a software tool WinSCP to transfer manually files between the GCS and the platform.

## Slide 6: Connecting to QCar
Once your files are transferred, you can deploy them via remote terminal using PuTTY tool

## Slide 7: Connecting to QCar
If your code requires graphical feedback such as displaying image processing results Xlaunch with an X11 server can be used.

## Slide 8: Connecting to QCar
3) The final method of remote access with the QCar is to use a remote desktop application such as VNC Viewer.

## Slide 9: SLAM
This example demonstrates how to implement the Simultaneous Localization And Mapping (SLAM) algorithm on a collected series of lidar scans to build a map of the environment.

## Slide 10: Manual Drive
We will capture commands from a Gamepad and use it to manually drive the QCar platform.
The application will also calculate the car’s speed from encoder counts.

## Slide 11: SLAM in ROS
We use a combination of the Hector SLAM packages, gamepad control node and LIDAR node.
Occupancy grid map generation can be viewed online or by replaying the saved ROS bag in rviz .

## Slide 12: SLAM in ROS
With super user authority run the slam.sh script which is in the ros1 folder.
The slam.sh file launches the file slam.launch.
The launch file runs the following nodes which are specific to the QCar: qcarnode.py, commandnode.py, and SLAMCorrected.py.

## Slide 13: Save and Load Lidar Data
Once the occupancy grid map was generated by the SLAM algorithm, we can save the RViz configuration in the directory ~/ros1/src/qcar/launch/slam.rviz.
You also can use this configuration setting to view the rosbag files of the previous experiments.

## Slide 14: Visualize the Constructed Map
We can use rviz to display the constructed map or rosbag files.

## Slide 15
SALM with MATLAB

## Slide 16
Obtaining Lidar Scans Data

## Slide 17: Thanks for Your Time

## Slide 18: Rights of use
This is shared under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International Public License