## Slide 1: Robot Operating System (ROS)
University of Windsor
Electrical and Computer Engineering Department
Mechatronics and Robotics Lab (MRL)
By: Saeed Mozaffari
2021

## Slide 2: Outline
What is ROS?
ROS installation
ROS Architecture
ROS command tools
ROS GUI tools

## Slide 3: Robot programming
A robot is a machine with sensors, actuators (motors), and a computing unit.

## Slide 4: Robot programming
Robot programming is programming the computing unit to perform a specific application using actuators and feedback from various sensors.
Robot programming is different from conventional programming because a robot has different input and output devices.
The input devices include robot sensors, teach pendants, and touch screens.
The output devices include LCD displays and actuators (motors).
Any programming language can be used to program robots, but C++ and Python are the most used languages.

## Slide 5: ROS
ROS is an open-source software framework that is used for robot-programming.
It facilitates communication between two programs or process.
The ROS project started at Stanford University in 2007.
Each version of ROS is called a ROS distribution.
ROS distributions include Noetic, Melodic, Kinetic, and so forth.
ROS 2.0 is a better version of the existing ROS in terms of security and real-time processing (https://github.com/ros2/ros2/wiki).

## Slide 6: ROS capabilities
Message passing interface between processes.
  Two programs (processes) can easily communicate with each other.
  For example, a camera and a line tracking algorithm can easily send information to each other.
Operating system–like features.
  Although ROS is not a real operating system, it provides some operating system functionalities such as multithreading, low-level device control, package management, and hardware abstraction.
  For example, with the hardware abstraction, we don’t need to rewrite the code when we use a new sensor from another vendor.
High-level programming language support.
  ROS supports popular programming languages including C++, Python, C #, Java, and so forth.
Availability of third-party libraries.
  With ROS framework we can use popular third-party libraries such as OpenCV (https://opencv.org) for robotic vision, and PCL (http://pointclouds.org) for 3D robot perception.

## Slide 7: ROS capabilities
Off-the-shelf algorithms.
  Available algorithms reduce development time for prototyping a robot.
  Example of off-the-shelf algorithms are SLAM (Simultaneous Localization and Mapping), and Dijkstra path planning.
Community support.
  ROS developers are actively developing and maintaining ROS packages.
  ROS Answers (https://answers.ros.org/questions/) and ROS Discourse (https://discourse.ros.org) are online forums in which ROS users discuss various topics and publish news related to ROS.
Extensive tools and simulators.
  ROS has GUI tools to debug, visualize, and simulate robotics applications.
  Examples include Rviz (http://wiki.ros.org/rviz) tool for visualization with cameras and laser scanners.
  Also, Gazebo (http://gazebosim.org) for robot simulations.

## Slide 8: ROS installation
First visit ROS installation page (http://wiki.ros.org/ROS/Installation).
Then select ROS Noetic which is long-term support (LTS) and compatible with ubuntu 20.04 which was installed before.

## Slide 9: ROS installation
Since ROS is not an operating system, it needs a host operating system to work.
Select your platform.

## Slide 10: ROS installation
1) Configure the Ubuntu repositories.
  To install ROS, we must enable access to the entire repository so that Ubuntu can retrieve packages from these repositories.
  Search in Ubuntu for “Software & Updates”.
  Then, enable the access of each repository.

## Slide 11: ROS installation
2) Set up your sources.list.
  Setup your computer to accept software from packages.ros.org.
  Execute the below command in your local shell:
    sudo sh -c 'echo "deb http://packages.ros.org/ros/ubuntu $(lsb_release -sc) main" > /etc/apt/sources.list.d/ros-latest.list'

## Slide 12: ROS installation
3) Set up your keys.
  Execute the following two commands in your local shell:
    sudo apt install curl # if you haven't already installed curl
    curl –s https://raw.githubusercontent.com/ros/rosdistro/master/ros.asc | sudo apt-key add –
4) Update the Ubuntu package list
  Execute the following commands:
      sudo apt update
      sudo apt upgrade

## Slide 13: ROS installation
5) Install ROS Noetic packages
  Install the Desktop-Full version which is recommended.
  Execute the following command:
    sudo apt install ros-noetic-desktop-full

## Slide 14: ROS installation
6) Environment setup
  To access these commandline tools and packages, we have to set up the ROS.
  Execute the following command:
    source /opt/ros/noetic/setup.bash
  This command should be run on every new shell you open to have access to the ROS commands.
  In order to automatically source this script every time a new shell is launched, we can add this line to your .bashrc file with the following command:
    echo "source /opt/ros/noetic/setup.bash" >> ~/.bashrc
  Next, enter the following command to add the environment in the current terminal.
    source ~/.bashrc

## Slide 15: ROS installation
7) Set up dependencies for building the package.
  If a robot has several packages, it is difficult to manage all the dependencies of those packages.
  rosinstall tool installs all the packages in a single command.
    Execute the following command:
      sudo apt-get install python-rosinstall python-rosinstall-generator python-wstool build-essential
8) Initialize rosdep
  rosdep tool is useful for installing the dependent packages of a ROS package.
  Execute the following commands:
    sudo rosdep init
    rosdep update

## Slide 16: ROS installation
9) Test your setup
  You can verify that your installation is correct by using the
  following command.
    rosversion –d
  If you get ‘Noetic’ as the output, you are all set with the installation.

## Slide 17: ROS Architecture
A ROS system is made up of many different programs running simultaneously and communicating with one another.
To perform such tasks, ROS is based on the following computation and communication unites:
ROS node: A process that performs computation. Think of it as one executable program.
  For example, obstacle recognition, and motor drive are nodes.
ROS master: An intermediate program that connects ROS nodes.
  The connection and communication between nodes
  are impossible without the master.

## Slide 18: ROS Architecture
ROS parameter server: A program that normally runs along with the ROS master.
  The user can store various parameters or values on this server and all the nodes can access it.
ROS topics: Named buses in which ROS nodes can send a message.
  A node can publish or subscribe any number of topics.
ROS message: The messages are basically the data going through the topic.
  There are existing standard messages.
  Users can also write their own messages.

## Slide 19: Example
Hello World Demo:
This is a basic ROS example which is already installed in ROS.
  There are two nodes: talker and listener.
  There is a topic called /chatter between two nodes.
  The talker node publishes a string message (Hello World ).
  The listener node subscribes it and prints it.

## Slide 20: Example
In order to have a communication between talker and listener nodes, the following message communication flow should be established.
1) Running the Master:
  The ROS master is run by using the roscore command and runs the server with XMLRPC.
  The master registers the name of nodes, topics, message types, URI addresses and ports for node-to-node connections.

## Slide 21: Example
2) Running the Subscriber Node:
  Subscriber nodes are launched with either a rosrun or roslaunch commands.
  The subscriber node registers its node name, topic name, message type, URI address, and port with the master as it runs.

## Slide 22: Example
3) Running the Publisher Node:
  Publisher nodes are also launched with either a rosrun or roslaunch commands.
  Like the subscriber node, the publisher node registers its information.

## Slide 23: Example
4) Providing Publisher Information:
  The master distributes the publisher node information to the subscriber node.

## Slide 24: Example
4) Connection Request from the Subscriber Node:
  The subscriber node requests a direct connection to the publisher node based on the publisher information received from the master.
  The subscriber node also transmits its information to the publisher node.

## Slide 25: Example
5) Connection Response from the Publisher Node:
  The publisher node sends the URI address and port number of its TCP server in response to the connection request from the subscriber node.

## Slide 26: Example
6) TCPROS Connection:
  The subscriber node creates a client for the publisher node using TCPROS (TCP/IP based protocol) and connects to the publisher node.

## Slide 27: Example
7) Message Transmission:
  The publisher node transmits a predefined message to the subscriber node through TCPROS.

## Slide 28: Example
Let’s run the Hello World demo in ROS:

## Slide 29: Example
Start the talker node by using the following command in another terminal:

## Slide 30: Example
Now start the listener node in another terminal:

## Slide 31: ROS Demo: turtlesim
In this demo we want to use a 2D simulator with a turtle in it.
  The turtlesim application is already installed on ROS.
  You can move the turtle with the keyboard, read the turtle’s current position, etc.

## Slide 32: ROS Demo: turtlesim
Start roscore.
In another terminal, run rosrun turtlesim turtlesim_node

## Slide 33: ROS Demo: turtlesim
To move the turtle, start turtle_teleop_key node from turtlesim package in another terminal.
When you press an arrow key, the node publishes velocity to /turtle1/cmd_vel.

## Slide 34: ROS Architecture Cont.
So far, we studied ROS node, ROS master, topics, and message.
There are other computation concepts such as ROS services, and ROS bags.
ROS Services: Unlike ROS topics, ROS service has Request/Reply mechanism.
  A service call is a function, which can call whenever a client node sends a request.
  The node who create a service call is called Server node and who call the service is called client node.
ROS bags: A useful method to save and play back ROS topics.
  It is useful for logging the data from a robot to process it later.

## Slide 35: Example
In the turtlesim demo there are some services.
In the following you can see the list of available services:
We can call a service by rosservice call command followed by the name of the service.

## Slide 36: Example
Let’s use spawn service, which duplicates a turtle at (x, y, theta) and returns the name of the turtle.

## Slide 37: ROS Command Tools
There are command-line tools in ROS which help us to leverage capabilities of ROS.
They should be executed in the Linux terminal.
rosnode list: it provides list of nodes running on the system.
rostopic list: it gives information about ROS topics, including publishers, subscribers, publishing rate, and ROS Messages.
rostopic echo: with this command we can dispaly the message in a topic.
rostopic pub: it can be used to publish a message in a topic. Name of the topic, the message type, and the message data should be stated. Format of this command is:

## Slide 38: Exercise
Take Hello World example into consideration.
  Show the list of its nodes.
  Show the list of topics in it.
  Print the published message in the topic.
  Publish another message in the topic.

## Slide 39: Solution

## Slide 40: ROS Command Tools Cont.
There are other command-line tools in ROS.
rosparam list: shows list of the parameters in the system.
rosparam get: gives you the value of the parameter.
rosparam set: we can change the value of the parameter.

## Slide 41: Example
Let’s see the parameters associated with the turtlesim and change some of them.

## Slide 42: ROS rqt Tools
The rqt tools is a graphical representation of ROS nodes, topics, messages, and other information.

## Slide 43: ROS rviz Tools
Using Rviz, we can visualize image data, 3D point clouds, and robot models, as well as transform data and so forth..

## Slide 44: Rights of use
This is shared under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International Public License